## Slide 1: CXL
I/O Interconnect
Accelerators and Memory devices
Multiple protocols
  Typical I/O – CXL.io, like PCIe
  Cache coherence – CXL.cache
  Memory access – CXL.memory

## Slide 2: CXL

## Slide 3: CXL – Is it revolutionarily new?
Not really. Same hardware stuff as PCIe 4.0/5.0
  64GBps (enough for a 400Gbps NIC) for PCIe 5.0
  Couldn’t get a hold of latency numbers. Heard ~400ns.

## Slide 4: FlexBus
CXL needs new support both on the processor and device-side.
FlexBus – kinda like a PHY layer that now supports both PCIe and CXL – but only one at a time.

## Slide 5: CXL Layers
Each protocol has its own implementation in every layer.

## Slide 6: CXL Device Types

## Slide 7: CXL.cache
Essentially another L1/L2 cache that host now needs to take care of.
Host/Device Bias mode, on page granularity
Performance?
  64B transactions

## Slide 8: CXL.mem
Mem read/writes while ensuring coherency
Specifies transaction flows in various situations

## Slide 9: How do we use it for remote memory?
Type 3 with just CXL.mem?
Is there going to be a NIC/ethernet?
No DRAM cache – would the usual L3 be enough?