## Slide 1: Aquila: A unified, low-latency fabric for datacenter networks
Dan Gibson, Hema Hariharan, Eric Lance, Moray McLaren, Behnam Montazeri, Arjun Singh, Stephen Wang, Hassan M. G. Wassel, Zhehua Wu, Sunghwan Yoo, Raghuraman Balasubramanian, Prashant Chandra, Michael Cutforth, Peter Cuy, David Decotigny, Rakesh Gautam, Alex Iriza, Milo M. K. Martin, Rick Roy, Zuowei Shen, Ming Tan, Ye Tang, Monica Wong-Chan, Joe Zbiciak, Amin Vahdat
Google

## Slide 2: Google’s history

## Slide 3: Datacenter Network (DCN) 101

## Slide 4: DCN Considerations
Topology
  Scalability
  Incremental deployment
  Cabling complexity
  Failure tolerance
Routing
  Maximizing bandwidth
  SDN Complexity
Transport
  Congestion control
  Low Latency

## Slide 5: Motivation
Need for ultra-low latency:
  Tightly-coupled DC workloads
  Low-latency RDMA
  Resource disaggregation
Goal: RDMA co-existing with TCP/IP but without performance impact
  RDMA on L3 – too slow
  RDMA on L2 – but ethernet makes sharing difficult
So why not rebuild L2 to support both?
Notes: The need for backward compatibility combined with challenges in deploying niche "bag on the side" networks threatens a new ossification in datacenter networking and distributed systems where we are left with programming to the lowest common denominator of TCP transports and commodity Ethernet switches with associated latency, CPU efficiency, and isolation limitations.

## Slide 6: Aquila
Clique-based architecture
  1-2k network ports per clique
  Plugs into the traditional clos network
  New capabilities within the Clique
    Robust RDMA
    Predictable, low-latency communication
    Device disaggregation
    Support for ML primitives
  Traditional IP-based transport between Cliques
  Sufficiently larger (than a rack) for many apps

## Slide 7: Aquila: Design goals
Cost-effective
  Single, replicated silicon component
  Switch in the NIC: ToR-in-NIC (TiN) chip
  Connections within and across Cliques
NIC + medium-radix switch
Notes: Combining NIC and ToR into the single TiN chip was a less costly path to innovation than separate NIC and switch ASIC programs

## Slide 8: Aquila: Design goals
Cost-effective
Ultra low-latency
  Cell-based communication – much smaller than packets
  Shallow-buffering
  Near lossless delivery – with end-to-end solicitation
Notes: Combining NIC and ToR into the single TiN chip was a less costly path to innovation than separate NIC and switch ASIC programs

## Slide 9: Aquila: Design goals
Cost-effective
Ultra low-latency
Unified fabric
  Both legacy and RDMA traffic
  New Layer-2 protocol GNet
  Bake RDMA into GNet, instead of overlay
Notes: Combining NIC and ToR into the single TiN chip was a less costly path to innovation than separate NIC and switch ASIC programs

## Slide 10: Aquila: Design goals
Cost-effective
Ultra low-latency
Unified fabric
Co-existence in the larger DCN
  Plugs externally with Ethernet
  Self-contained SDN controller
  Clique-locality in Job scheduling
Notes: Combining NIC and ToR into the single TiN chip was a less costly path to innovation than separate NIC and switch ASIC programs

## Slide 11: Overview
Hardware design and layout
SDN Infrastructure & Challenges
Results
Limitations/Discussion

## Slide 12: TiN Chip
50-port Cell Switch
  24 pod-local links (copper)
  8 inter-pod links (optical)
  18 internal (IP, RDMA, etc.)
  32 VCs with FIFO per port
  Credit-based Flow Control
  Isolated buffers/credits

## Slide 13: TiN Chip
GNet L2 protocol on all links
  Cell size 16 to 160B
  8B header
    16-bit source and destination address
    Cell type, VC, hop count, CRC, etc.
  Adaptive routing for most traffic
    Minimal & Non-minimal routes
    Randomized, weighted route picking
    Deterministic only for ordered traffic

## Slide 14: IP over GNet
IP to GNet translation
  Sources: NIC & External Ethernet
  Split IP packets to cells
  Gather then back at destination
  L3 to L2 address translation

## Slide 15: IP over GNet
Admission control
  Solicitation with RTS/CTS
  On high-priority VC
  Routed deterministically
  RTS order defines packet order
  Packet Drops/ECN at ingress based on RTS queue thresholds
  CTS window can be adaptively controlled to ease congestion
Helps with incast at receiver/RTS path but what about other points in the fabric?

## Slide 16: RDMA over GNet
1RMA – Google’s RDMA variant
  Not layered on IP anymore
  First-class cell types: Req, Resp
  Similar treatment as RTS/CTS
  Gets separate VCs
  No HOL-blocking by IP traffic

## Slide 17: Logical Layout
Set of TiNs form a pod (rack)
Set of pods, an Aquila clique

## Slide 18: Physical Layout

## Slide 19: SDN Infrastructure
Centralized Control Plane
  Aquila-wide controller
Embedded Control Processor
  In each TiN
  Wimpy for cost reasons
  Exposes low-level register API
Notes: The TiN chip has an embedded control processor (ECP) to handle all switch side control and monitoring actions. Cost of silicon exerts pressure to make the ECP as simple as possible, as it is replicated in each TiN chip. Where a typical control processor for a ToR might be a multicore, 64-bit processor with 8-16 GB of memory, TiN’s ECP is a 32-bit ARM Cortex M7 processor with a mere 2 MB of SRAM.

## Slide 20: SDN Challenges for Aquila
Exploded routing state (for SDN controller)
  Large number of endpoints and routing tables
  Hierarchical naming and pruning redundant rules
  Routing table in the TiN chip, what if it overflows?
Notes: The TiN chip has an embedded control processor (ECP) to handle all switch side control and monitoring actions. Cost of silicon exerts pressure to make the ECP as simple as possible, as it is replicated in each TiN chip. Where a typical control processor for a ToR might be a multicore, 64-bit processor with 8-16 GB of memory, TiN’s ECP is a 32-bit ARM Cortex M7 processor with a mere 2 MB of SRAM.

## Slide 21: SDN Challenges for Aquila
Exploded routing state
Switch firmware w/ 2MB SRAM
  With FreeRTOS & lwIP net stack
  Minimal functionality
  Low level API to chip registers
  Stateless firmware
Notes: The TiN chip has an embedded control processor (ECP) to handle all switch side control and monitoring actions. Cost of silicon exerts pressure to make the ECP as simple as possible, as it is replicated in each TiN chip. Where a typical control processor for a ToR might be a multicore, 64-bit processor with 8-16 GB of memory, TiN’s ECP is a 32-bit ARM Cortex M7 processor with a mere 2 MB of SRAM.

## Slide 22: SDN Challenges for Aquila
Exploded routing state
Switch firmware w/ 2MB SRAM
In-band bootstrapping
  TCP connections to TiNs in waves
  Border TiNs connect first over DCN links
  Other TiNs proxy through neighbors
    Adjacent TiNs talk over PMOS protocol
  DHCP and Control messages over GNet and PMOS
  3 to 48 mins for TiN bootstrap
Notes: The TiN chip has an embedded control processor (ECP) to handle all switch side control and monitoring actions. Cost of silicon exerts pressure to make the ECP as simple as possible, as it is replicated in each TiN chip. Where a typical control processor for a ToR might be a multicore, 64-bit processor with 8-16 GB of memory, TiN’s ECP is a 32-bit ARM Cortex M7 processor with a mere 2 MB of SRAM.

## Slide 23: Evaluation
Testbed 1 Aquila Clique: 578 TiNs, 500 hosts
Apps
  IP traffic generator using Pony Express [1]
  CliqueMap [2]: An KV store using Pony Express or 1RMA
  Both use Swift [3] Congestion Control
Metrics
  IP Fabric RTT
  1RMA Total Execution Latency
  Achieved throughput
[1] Snap: a microkernel approach to host networking, SOSP’19
[2] CliqueMap: productionizing an RMA-based distributed caching system, SIGCOMM’21
[3] Swift: Delay is Simple and Effective for Congestion Control in the Datacenter, SIGCOMM’20

## Slide 24: Latency under load
IP
1RMA

## Slide 25: Latency Isolation

## Slide 26: Application Impact

## Slide 27: Limitations
DragonFly doesn’t allow incremental deployment (on rack scale)
Allows lesser radius
Debugging cell-switched network
No improvements for legacy applications

## Slide 28: Discussion
How else could they have evaluated?

## Slide 29: Aquila Summary
First attempt at DCN that supports emerging technologies at scale
Clique-scale resource disaggregation
Clique-scale ultra low-latency apps
With backwards compatibility